## Slide 1
Modernization of Special
Airworthiness Certification
(MOSAIC)
Pilot Certification and Operations
Presented to: SMASH
By: Seth Lake
Date: 12/08/2025
Federal Aviation
Administration
Notes: 2025/10-22-55(E)PP Original Author: AFS-810 22 October 2025; POC John Steuernagle National FAASTeam Operations Program Manager, Office 562-264-5484
Presentation Note: This is the title slide for Modernization of Special Airworthiness Certification (MOSAIC).
Presentation Note: This is the only permissible MOSAIC presentation for FAASTeam Program Managers and their Reps. With the exception of Slide 27 as needed, no modifications are authorized.
Script - We have included a script of suggested dialog with most slides. The script will always appear in a non-italic font. Presenters may read the script or modify it to suit their own presentation style. See template slides 5 and 6 for examples of slides with script.
Presentation Instructions - (stage direction and presentation suggestions) will be preceded by a Bold header: the instructions themselves will be in Italic fonts.
Program control instructions - will be in bold fonts and look like this: (Click) for building information within a slide; or this: (Next Slide) for slide advance.
Background information - Some slides may contain background information that supports the concepts presented in the program. Background information will always appear last and will be preceded by a bold Background: identification.
The production team hope you and your audience will enjoy the show. Break a leg!
(Next Slide)

## Slide 2: Overview
Summary of changes from previous requirements
Effective dates
Final rule details pertaining to pilot training and testing
Final rule part 91 changes
MOSAIC references
Notes: Welcome to a discussion of FAA’s Modernization of Special Airworthiness Certification or MOSAIC.
In this presentation we’ll summarize change from previous requirements. We’ll discuss effective dates, final rule details pertaining to pilot training and testing. Changes to 14CFR 91, and
finally, we’ll provide some MOSAIC references.
(Next Slide)

## Slide 3: MOSAIC Final Rule Pilot Certification Provisions (14 CFR Part 61)
This rule separates light sport category aircraft certification requirements from the sport pilot certification requirements and removes the former § 1.1 light-sport aircraft definition.
Additionally, the rule expands what aircraft sport pilots can operate and adds operational privileges that require additional training and qualification.
The rule also adds make and model specific training and endorsement requirements for pilots seeking to act as PIC of aircraft with the simplified flight controls designation.
Notes: These are the major areas of change affecting sport pilots, flight instructors with a sport pilot rating, and pilots with a higher-grade certificate when exercising sport pilot privileges. (Click)
We’ve separated light sport aircraft certification requirements from sport pilot certifications and removed the light-sport aircraft definition. (Click)
We’ve expanded what aircraft sport pilots can operate and added operational privileges that require additional training and qualification. (Click)
And we’ve added make and model specific training and endorsements for pilots seeking to act as PIC of aircraft with a simplified flight controls designation. At present there are no aircraft with this
(Next Slide)

## Slide 4: MOSAIC Final Rule Dates
MOSAIC final rule was published on July 24, 2025, with two effective dates:​
October 22, 2025 (90 days after publication)​
  Pilot rules and privileges​
  Repairman certification, maintenance rules, and tow-hitch installation​
  Class G airspace and right-of-way rules​
July 24, 2026 (365 days after publication)​
  Removal of “light-sport aircraft” definition from 14 CFR § 1.1​
  Airworthiness certification requirements​
  Changes in operations, including operating limitations ​
Notes: The final rule was published in July with two effective dates. (Click)
On October 22, 2025, we saw changes to pilot rules and privileges, repairman certification, maintenance, and tow-hitch installation, Class G airspace and right-of-way rules. (Click)
In July of 2026, we’ll remove the light-sport aircraft definition from 14CFR § 1.1. You’ll see changes to Airworthiness certification requirements and changes in operations, including operating limitations.
(Next Slide)

## Slide 5: MOSAIC Part 61 Changes
Notes: (Next Slide)

## Slide 6: New Aircraft Limitations for Sport Pilots
The MOSAIC final rule removes “light-sport aircraft” definition from 14 CFR part 1.1. Revised aircraft design and performance limitations for sport pilots are listed in the new 14 CFR § 61.316. Here are some of the changes to the aircraft limitations:
Removal of the aircraft weight and speed limitation
Use of any powerplant type except turbo-jet
New maximum Vs1 stall speed of 59 knots CAS for airplanes, flaps retracted
Allows use of 4 seat airplanes, but retains 2 occupant limitation
Can operate aircraft with a retractable gear
Can operate airplanes with manual controllable pitch propeller
New rotorcraft-helicopter privilege (only those equipped and certificated with the simplified flight controls designation)
Notes: (1) With the changes introduced in the MOSAIC rule, sport pilots are no longer limited to only operating light-sport aircraft as previously defined in § 1.1. This definition will be removed with the new rule as of July 24, 2026.
With this change, the FAA transitioned the aircraft design and performance limitations for the aircraft sport pilots can operate to part 61. The new § 61.316 prescribes these limitations.
As of the October 22, 2025, effective date of the rule, sport pilots (and pilots with a higher-grade pilot certificate exercising sport pilot privileges) may operate aircraft that meet the § 61.316 performance and design limitations.
It is important to note that aircraft may still be certified as light-sport category aircraft, however an aircraft in this certification category may not inherently meet the new § 61.316 performance and design limitations. In other words, some aircraft certified in the light-sport category may not be eligible for sport pilot operations. Sport pilots may only operate aircraft meeting the § 61.316 limitations regardless of the aircraft certification category. Similarly, flight instructors with a sport pilot rating may only provide flight training in an aircraft that meets the § 61.316 limitations.
(2) Let’s take a closer look at the § 61.316 performance and design limitations. (Click)
Many of the former § 1.1 “light-sport aircraft” criteria have been incorporated into the new § 61.316. However, there are some notable changes:
There is no longer a prescribed weight or speed limitation for the aircraft a sport pilot may operate.
There is no limitation on powerplant type for the aircraft a sport pilot may operate. However, a sport pilot may not operate an aircraft requiring a pilot type rating and therefore cannot operate a turbojet powered aircraft.
The maximum stalling speed or minimum steady flight speed without the use of lift-enhancing devices (VS1) has been increased for airplanes. A sport pilot may operate airplanes with a VS1 speed of 59 knots calibrated airspeed (CAS) or less.
  Glider and weight shift control aircraft categories retain the maximum VS1 of 45 knots CAS for sport pilot operations.
Under the new rule, a sport pilot may operate an airplane with a seating capacity of four persons. Other aircraft categories allow a maximum seating capacity of two persons.
  Regardless of seating capacity, a sport pilot may not act as pilot in command while carrying more than one passenger.
Sport pilots are permitted to act as pilot in command of an aircraft with retractable landing gear or a manual controllable pitch propeller.
  These privileges require specific additional training and endorsement. We will look at these more closely in an upcoming slide.
The new rules (as accommodated by § 61.316) allow a new rotorcraft-helicopter privilege (only those equipped and certificated with the simplified flight controls designation) for sport pilots. We will also look at this in more detail.
(3) Finally, it is important to note that the § 61.316 performance and design limitations require the aircraft to have met those criteria “since its original certification.”
In other words, an aircraft that did not meet § 61.316 limitations at the time of its original certification may not be brought into compliance through modifications made after that original certification.
  For example, an airplane with six seats that has had seats removed to two seats (leaving four remaining seats) would not qualify for sport pilot operations.
  Similarly, an airplane originally certified with a maximum VS1 stalling speed greater than 59 knots CAS would not qualify for sport pilot operations even if that aircraft had aftermarket modifications lowering that stalling speed.
(Next Slide)

## Slide 7: New Aircraft Limitations for Sport Pilots
§ 61.316(a) If you hold a sport pilot certificate, you may act as pilot in command of an aircraft that, since its original certification…
“Since Original Certification” requirement:
  Modifications to aircraft to reduce the Vs1 speed after its original certification cannot qualify an airplane for sport pilot use.
  Modifications to reduce seating capacity after its original certification cannot qualify for sport pilot use.
Notes: Here’s some additional detail on Original Certification. (Click)
  Aircraft Conformity Since Original Aircraft Certification. The § 1.1 Light-sport aircraft definition previously required an aircraft to have met all design requirements since its original certification. The MOSAIC final rule retains the “since its original certification” requirement for aircraft performance and design requirements in new § 61.316(a).
  Sport pilots cannot operate an aircraft that has been modified since its original certification to otherwise qualify an aircraft for sport pilot use under § 61.316(a).
  Modifications to an aircraft to meet § 61.316(a) criteria may allow operation of aircraft with overall increased complexity to a level that is inappropriate for the skill and training capabilities of the sport pilot.
  Therefore, sport pilots may only act as PIC of an aircraft meeting the performance limits and design requirements of § 61.316(a) if that aircraft meets those requirements since its original certification.
  Modifications made after original certification cannot be used to qualify an aircraft for sport pilot use under § 61.316.
(Next Slide)

## Slide 8: Separate Stall Speed Limitations
  The pilot certification section of the final rule established a maximum Vs1 CAS stalling speed of 59 knots under § 61.316, to indirectly limit the weight and cruise speed for airplanes that a sport pilot can operate without using a prescriptive weight limit.
  The aircraft certification section adopted an independent 61 knot Vso maximum stalling speed limit for the certification of light-sport aircraft under § 22.100. This allowed for a significant expansion of what aircraft can be certificated using consensus standards under part 21.
Notes: FAA identified NTSB accident data that shows there were more fatalities in the departure phase (takeoff and initial climb, VS1 no flaps configuration) than in the arrival phase (approach and landing, VS0, flaps configuration). NTSB states that takeoff begins at the application of takeoff power and the initial climb ends upon reaching enroute (cruise) altitude and the landing phase begins at flare and ends when the aircraft comes to a stop or exits the runway. Given the accident data from the NTSB and that departure for most light sport aircraft occurs in a VS1 configuration, FAA has determined that using a VS1 maximum stalling speed limitation is more appropriate for indirectly limiting what aircraft sports pilots can operate because more fatalities occur in the departure phase (VS1 configuration).
MOSAIC separates pilot certification and operational requirements from aircraft certification. This briefing focusing on sport pilot certification and privileges and, as discussed, § 61.316 establishes performance and design requirements for the aircraft sport pilots may operate. It is important to understand that for the purposes of light sport aircraft certification, different criteria area used due to different priorities in aircraft certification. Specifically, § 22.100 uses Vs0 of 61 knots.
As a result, this final rule revises the existing maximum VS1 CAS stalling speed to 59 knots to indirectly limit cruise speed and other performance characteristics of airplanes that a sport pilot can operate, whereas use of the VS0 maximum stalling speed of 61 knots, at a minimum, would then substantially increase the VS1 stalling speed and further expand the performance characteristics of these airplanes. In turn, this would inappropriately permit sport pilots to operate larger, faster, and more complex airplanes outside the scope of their minimal training and experience requirements that a sport pilot receives. Using VS1 CAS more effectively limits airplane performance characteristics to the training and skills expected of a sport pilot rather than a maximum VS0 stalling speed limitation of 61 knots, which would permit airplanes with greater overall performance characteristics, thereby necessitating a greater level of pilot training and proficiency validation.
Sport pilots are no longer limited to operating “light-sport aircraft” but similarly, not all newly certified light-sport aircraft will meet § 61.316 to be eligible for sport pilot operations because of this separation between pilot requirements and aircraft certification requirements. A light-sport airplane with a VS1 greater than 59 knots could not be operated using sport pilot privileges.
(Next Slide)

## Slide 9
VS1
VSO
(Clean)
(Configured)
61CAS
52CAS
RV-10

## Slide 10
VS1
(Clean)
CAS
Sport Pilot:
VS1
CAS Limit
(Clean)
RV-10
61 > 59
61
59

## Slide 11
VSO
(Configured)
CAS
Sport Category:
VSO
CAS Limit
(Configured)
RV-10
52 < 61
52
61

## Slide 12
VS1
VSO
(Clean)
(Configured)
68CAS
58CAS
A36

## Slide 13
VS1
(Clean)
CAS
Sport Pilot:
VS1
CAS Limit
(Clean)
A36
68 > 59
68
59

## Slide 14
VSO
(Configured)
CAS
Sport Category:
VSO
CAS Limit
(Configured)
A36
58 < 61
58
61

## Slide 15
VS1
VSO
(Clean)
(Configured)
56CAS
50CAS
RG182

## Slide 16
VS1
(Clean)
CAS
Sport Pilot:
VS1
CAS Limit
(Clean)
RG182
56 < 59
56
59

## Slide 17
VSO
(Configured)
CAS
Sport Category:
VSO
CAS Limit
(Configured)
RG182
50 < 61
50
61

## Slide 18
RG182
Sport Pilot Endorsements
61.331 & 61.31(e)

## Slide 19: Vs Speed Determination
Review the aircraft type certificate data sheet (TCDS) or flight manual for the stall speed at the time of aircraft certification.
Vs1 cannot be more than 59 knots CAS.
  Note: To find the TCDS, go to drs.faa.gov and type in TCDS in the search bar on left side. Pick the aircraft manufacturer and type of airplane.
Notes: It is the responsibility of the pilot to determine if their airplane meets the requirements listed in § 61.316. Pilots should review the aircraft type certificate data sheet (TCDS) or flight manual for the stall speed at the time of aircraft certification.
Each make and model is different and there may be further variations in aircraft series.
The pilot may need to contact the manufacturer to determine if their specific make, model and series of aircraft qualifies under § 61.316 if insufficient information is available.
(Next Slide)

## Slide 20: New Operational Privileges for Sport Pilots
Aircraft with a retractable landing gear;
Airplanes with manual adjustable pitch propeller; and
Night operations using Basic Med or FAA medical qualification requirements.
Note: Additional training and instructor qualifying endorsements are required for these additional (but optional) sport pilot operating privileges.
Regulations: § 61.316(b), § 61.331, § 61.329
Notes: In addition to the new optional privileges allowing sport pilots to operate aircraft with retractable landing gear or airplanes with a manual adjustable pitch propeller, the MOSAIC final rule adds new optional night operational privileges.
Additional training and instructor qualifying endorsements are required to exercise any of these optional privileges. Additionally, the night operational privileges require the pilot to hold an FAA medical certificate or BasicMed.
We will look at each privilege separately in the following slides.
(Next Slide)

## Slide 21: New Sport Pilot Night Operations Privilege § 61.329
Sport pilots can now conduct night operations after obtaining additional category and class specific night training experience.
  3 hours of night flight training in the specific category and class from an authorized instructor that includes-
    At least one cross country with a landing at least 25 nm from departure point
    10 takeoffs and landings to a full stop at night
Sport pilots are required to have at least a valid third-class medical certificate or meet the requirements of Basic Med (§ 61.23(c)(3)) to operate at night.
Must receive a logbook endorsement from an authorized instructor certifying that they meet training requirements in specific category and class.
* A private pilot or higher may count night experience but will still need instructor endorsement under § 61.329(c).
Notes: Why we added night to sport pilot operations. the FAA identified a risk where pilots may feel pressure to conduct flights before the end of evening civil twilight, especially in many northern states with reduced daylight hours. To appropriately mitigate night operations, especially with the expanded aircraft characteristics that a sport pilot can operate, FAA maintains that additional night training, an authorized instructor qualifying endorsement, and additional medical qualifications are necessary.
(Next Slide)

## Slide 22: New Sport Pilot Night Operations Privilege
Sport pilots can now conduct night operations after obtaining additional category and class specific night training experience and a qualifying flight instructor endorsement.
Sport pilots are required to have at least a valid third-class medical certificate or meet the requirements of Basic Med (§ 61.23(c)(3)) to operate at night.
Regulation: § 61.329
Notes: A sport pilot may act as pilot in command of an aircraft that meets the § 61.316 performance and design limitations at night if they meet the training, endorsement and medical certificate requirements of § 61.329.
Training requirements (§ 61.329(a))
- Receive 3 hours of night flight training in the specific category and class from an authorized instructor that includes-
(1) At least one cross-country flight at night, with a landing at an airport of at least 25 nautical miles from the departure airport (except for powered parachutes); and
(2) Accomplish at least 10 takeoffs and 10 landings to a full stop at night.
Required Endorsement § 61.329(c)
Must receive a logbook endorsement from an authorized instructor certifying the required training has been met and the pilot is proficient in the operation of the aircraft at night in the category and class of privileges sought.
Medical Requirement § 61.329(b)
- The pilots must either hold an FAA-issued medical certificate or meet the conditions of BasicMed (§ 61.113(i)). If utilizing BasicMed, the regulation makes clear that a sport pilot must comply with § 61.316 where the requirements of § 61.316 conflict with § 61.113(i). This means sport pilots may only operate an aircraft that meets the § 61.316 design and performance limitations even while exercising night privileges with BasicMed.
Pilots with Higher-Grades of Certificates
The MOSAIC final rule preamble addressed the scenario of a pilot with a higher-grade pilot certificate who chooses to exercise sport pilot privileges and wishes to conduct the optional night privileges. The FAA clarified that a person who holds a private pilot certificate (or greater) may apply their previous night training experience to meet the training requirements in § 61.329(a). However, when exercising the privileges of a sport pilot certificate and operating at night, they must have obtained the requisite endorsement under § 61.329(c) even if the pilot holds a higher grade of pilot certificate. Additionally, they must still meet the medical requirements of § 61.329(b) to exercise night privileges.
(Next Slide)

## Slide 23: New Sport Pilot Retractable Gear Operations Privilege
MOSAIC permits sport pilots to act as PIC of an aircraft with retractable landing gear. Pilots are required to have specific training and an endorsement prior to operating an aircraft with retractable landing gear.
Sport pilots have two options to comply with these requirements:
  A sport pilot may satisfy the training and endorsement requirements required for operating complex airplanes as specified in § 61.31(e); or
  A sport pilot may receive and log ground and flight training from an authorized instructor in an aircraft that has retractable landing gear and receive an endorsement from the instructor certifying that they are proficient to operate that aircraft.
Regulations: § 61.316(b), § 61.331(a),
Notes: A sport pilot may operate an aircraft with retractable gear by either:
Satisfying the § 61.31(e) complex airplane training and endorsement. This may be accomplished in an aircraft that meets the § 61.1 definition of a complex airplane (i.e., an airplane that has a retractable landing gear, flaps, and a controllable pitch propeller); or
Receive and log ground and flight training from an authorized instructor in an aircraft that has retractable landing gear and receive an endorsement from the instructor certifying that they are proficient to operate the aircraft (§ 61.331(a)(2)). This option accommodates privileges in aircraft that do not meet the full definition of “complex airplane.” It applies to any aircraft with retractable landing gear.
(Next Slide)

## Slide 24: New Sport Pilot Manual Pitch Propeller Privilege
MOSAIC permits sport pilots to act as PIC of an airplane with a manual controllable pitch propeller. Pilots are required to have specific training and endorsement requirements prior to operating an airplane with a manual controllable pitch propeller.
Sport pilots have two options to comply with these requirements:
  A sport pilot may satisfy the training and endorsement requirements required for operating complex airplanes as specified in § 61.31(e); or
  A sport pilot may receive and log ground and flight training from an authorized instructor in an airplane that has a manual controllable pitch propeller and receive an endorsement from the instructor certifying that they are proficient to operate the airplane.
Regulations: § 61.316(b), § 61.331(b),
Notes: A sport pilot may operate a manual controllable pitch propeller airplane by either:
Satisfying the § 61.31(e) complex airplane training and endorsement. This may only be accomplished in an aircraft that meets the § 61.1 definition of a complex airplane (an airplane that has a retractable landing gear, flaps, and a controllable pitch propeller).
Receive and log ground and flight training from an authorized instructor in airplane that has a manual controllable pitch propeller and receive an endorsement from the instructor certifying that they are proficient to operate the aircraft (§ 61.331(a)(2)). This option accommodates privileges in aircraft that do not meet the full definition of “complex airplane.” It applies to any airplane with a manual controllable pitch propeller.
A manual controllable pitch propeller is one that the pilot must set the pitch manually while operating the aircraft. A typical example of a manual controllable propeller is an aircraft with a constant speed propeller system, where the pilot adjusts propeller pitch with an RPM control and the propeller RPM is maintained by a propeller governor.
Manual controllable pitch propellers do not include automated controllable pitch propellers which operate without the pilot’s ability to manually control propeller pitch. Manual controllable pitch propellers also do not include ground-adjustable propellers with no manual pilot control in flight. Consequently, sport pilots are permitted to operate all adjustable-pitch propellers (automated, ground adjustable, or manual) but only requires pilots of airplanes with manual controllable pitch propellers and aircraft to receive additional training and an instructor qualifying endorsement.
(Next Slide)

## Slide 25: Subpart K CFI Limitations § 61.415
If you hold a flight instructor certificate with a sport pilot rating, you may only provide flight training in an aircraft meeting the performance limits and design requirements of § 61.316 and are subject to the following limits:
(k) Cannot carry more than one person.
(l) requires a flight instructor to have received the training and endorsement in an airplane with a manual controllable pitch propeller or an aircraft with a retractable landing gear aircraft prior to providing flight instruction in those aircraft.
  Do this by complying with § 61.331 or § 61.31.
Notes: In addition to the already published limitations, the FAA clarified or added to the requirements/
Updated the regulation to remove reference to § 1.1.
Clarified that may only have student and self onboard, no matter the number of seats installed.
A subpart K instructor must be qualified themselves prior to providing training in a retractable gear aircraft or manual controllable pitch airplane.
(Next Slide)

## Slide 26: New Sport Pilot CFI Night Operations Privilege § 61.415(n)
Qualifications to provide night flight training to sport pilots
  Any subpart H flight instructor
  Any subpart K flight instructor
    Must complete the required training and receive the § 61.329 endorsement in specific category and class.
A subpart K instructor can receive training from a subpart H instructor or another subpart K instructor that is qualified
Notes: The NPRM proposed to permit a person to receive the night training and endorsement specified in § 61.329 from an authorized instructor: a person who holds either a flight instructor certificate issued under subpart H of part 61 or a flight instructor certificate with a sport pilot rating under subpart K. Subpart H flight instructors receive training and validation of proficiency via testing on night operations to receive their certificate and are therefore qualified to provide flight training at night. For example, the Flight Instructor for Airplane ACS includes various night operations tasks and elements (e.g., Task M: Night Operations in Area of Operation II: Technical Subject Areas, which includes knowledge, risk management, and skills specifically key to night operations). This final rule adopts the proposal permitting subpart H instructors to provide § 61.329-night flight training.
(Next Slide)

## Slide 27: Subpart K CFI Privileges § 61.413
A flight review or operating privilege for a sport pilot, or training to maintain or improve the skills of a sport pilot.
(d) A person who holds a flight instructor certificate issued under subpart K may receive compensation for providing flight training in accordance with this subpart.
Notes: Emphasize subpart K instructors may only provide training or endorsements to sport pilots, students seeking a sport pilot certificate or privileges, a flight instructor certificate with a sport pilot rating.
The only change to existing § 61.413 privileges was to add a provision that allows a subpart K instructor to receive compensation for providing flight training in accordance with this subpart.
(Next Slide)

## Slide 28: Sport pilot certificate privileges
Airplane single engine land or sea class
Glider category
Rotorcraft gyroplane
Lighter-than-air airship
Lighter-than-air balloon
Powered parachute
Weight Shift Control
Rotorcraft Helicopter with simplified flight controls designation only
Notes: These are the only privileges available to a sport pilot at this time.
(Next Slide)

## Slide 29: Sport pilot certificate privileges
No powered-lift sport pilot privilege was created.
What is simplified flight controls (SFC)? This will be determined by AIR during aircraft certification. As of today, there are no aircraft certified with such designation and no determination has been made on what SFC will look like.
Notes: The FAA elected to not include a powered-lift sport pilot at this time due to the newness of powered-lift in the NAS. This will be a consideration for the future.
What are “simplified flight controls”?
This designation is issued during the aircraft’s certification. These designs differ from traditional or conventional flight controls. They are intended to be simpler for the pilot to operate and typically involve greater levels of automation. The simplified flight control design will vary between different aircraft makes and models. Consequently, due to this nature of aircraft with simplified flight controls, specific training and certification requirements are necessary. We will discuss how this impacts sport pilot certification in helicopters with simplified flight controls in an upcoming slide.
(Next Slide)

## Slide 30: New Sport Pilot Rotorcraft-Helicopter Privilege
New Sport Pilot Helicopter Privilege with Simplified Flight Controls Design Requirement
Allows sport pilots to obtain a rotorcraft helicopter privilege but restricted to those equipped with simplified flight controls.
New requirements for flight instructors with a sport pilot rating (Subpart K) seeking to conduct training in helicopters with simplified flight controls.
Regulations: § 61.311, § 61.313(a)(9), § 61.409, § 61.411(h)
Notes: The MOSAIC final rule has a new rotorcraft-helicopter privilege for sport pilots. However, sport pilots may only operate a helicopter with a simplified flight controls designation.

## Slide 31: Practical Test Required When Adding an Airplane or Helicopter Privilege
A sport pilot “proficiency check” can no longer be used to add an airplane (or new helicopter) privilege to an existing sport (or higher grade) pilot certificate.
The FAA now requires sport pilots and flight instructors with a sport pilot rating seeking to add an airplane (or new helicopter privilege) to their existing pilot or flight instructor certificate to successfully accomplish a practical test with a designated pilot examiner. Regulations: § 61.321(b), § 61.419(e)
Notes: Before we further discuss helicopters with simplified flight controls, let’s look at one rule change with a broader impact.
Historically, sport pilots add additional aircraft category or class privileges by completing a proficiency check. This check can be accomplished by an authorized instructor. Although sport pilot proficiency checks are retained for most categories and classes of aircraft, the MOSAIC rule makes a notable change for airplane and the new helicopter privilege.
As of the October 22. 2025, effective date of the new rule, a person who holds a sport pilot certificate or a flight instructor certificate with sport pilot rating who seeks to add an airplane (or new helicopter privilege) must successfully accomplish a practical test with a designated pilot examiner. Similarly, a pilot with a higher-grade certificate seeking to add airplane or helicopter privileges at the sport pilot level must accomplish a practical test with a designated examiner.
(Next Slide)

## Slide 32: Simplified Flight Controls Model-Specific Training and Instructor Endorsement Requirement
Pilots seeking to act as PIC of an aircraft with a simplified flight controls designation must obtain model-specific training and a qualifying instructor endorsement for each specific make and model aircraft. Pilots must already have the appropriate category and class rating or privilege before obtaining the simplified flight controls instructor qualifying endorsement. Regulation: §61.31(l)
Notes: Due to the unique characteristics and designs of each aircraft with simplified flight controls, model-specific training and a qualifying instructor endorsement are required for each specific make and model aircraft, as required by §61.31(l).
Pilots who already hold the appropriate category and class rating or privilege need only obtain the model-specific training and endorsement. A qualified flight instructor may provide this training and endorsement. Pilots who already hold the appropriate category and class rating or privilege do not need to complete a practical test to obtain the simplified flight controls model-specific endorsement.
However, pilots who do not hold the appropriate category and class rating or privilege must complete a practical test with a designated pilot examiner. [This is discussed further in the next slide.]
(Next Slide)

## Slide 33: Practical Tests conducted in Aircraft with Simplified Flight Controls Designation
Testing in Simplified Flight Controls Aircraft: Pilot applicants who complete the training and practical test in an aircraft equipped with simplified flight controls will receive a “make and model” simplified flight controls limitation on their pilot certificate.
Regulations: § 61.45(g)(4), § 61.45(h)
Note: Pilots who are issued a category and class rating (or privilege) with a simplified flight controls make and model limitation can have that limitation removed by accomplishing an additional practical test in the same category and class of aircraft equipped with “conventional” flight controls. [§ 61.45(h)(2)]
Notes: As we just established, if a person seeks a make and model authorization for an aircraft with a simplified flight controls designation and does not hold the category or class rating or privilege on their pilot certificate, they must successfully pass a practical test with a designated pilot examiner to receive that category and class rating or privilege to act as pilot in command of that aircraft.
In this scenario, a pilot applicant who completes the practical test in an aircraft equipped with simplified flight controls will receive a “make and model” simplified flight controls limitation on their pilot certificate. Consequently, the pilot’s privileges in that category and class of aircraft are limited to that make and model.
If that pilot later wishes to act as pilot in command of an aircraft of that category and class with “conventional” flight controls, they may have the make and model limitation removed by accomplishing an additional practical test in the same category and class of aircraft equipped with “conventional” flight controls.
(Next Slide)

## Slide 34: Training Requirements for Pilots Seeking to Operate Another Make and Model of Aircraft with a Simplified Flight Controls
Pilots seeking to operate another make and model of aircraft with a simplified flight controls designation (in the same category and class) must receive additional training and an endorsement prior to operating as PIC.
Regulation: § 61.45(h)(1)
Notes: Because the training and endorsement requirements to operate an aircraft with a simplified flight controls designation are make and model specific, a pilot who seeks to act as PIC of a different make and model of aircraft with a simplified flight controls designation (in the same category and class) must receive additional training and an endorsement.
Since the pilot in this scenario seeks to operate another make and model aircraft in the same category and class for which they already hold the appropriate category and class rating or privilege, a qualified flight instructor may provide the training and endorsement. An additional practical test would not be required.
However, if a pilot seeks to operate a new make and model of aircraft with a simplified flight controls in a different category and class, a practical test is required if they do not already hold that category and class rating or privilege.
(Next Slide)

## Slide 35: Inapplicability of Pilot Experience Credit in Simplified Flight Controls Aircraft
Limits pilot experience credit obtained in an aircraft with the simplified flight controls designation from satisfying flight time experience requirements for a higher-grade of pilot certificate. Regulation: §61.9
Exception: private pilot applicants who present an aircraft with the simplified flight controls designation to conduct the practical test
Notes: Except for private pilot applicants who present an aircraft with the simplified flight controls designation for their practical test, pilot time acquired while operating an airplane or helicopter with a simplified flight controls designation may not be used to satisfy certain aeronautical experience requirements for a private, commercial, or airline transport pilot certificate. According to § 61.9, pilot time in an aircraft with simplified flight controls may not be used to satisfy:
The solo flight time requirements for a private pilot certificate with an airplane single engine land or helicopter rating. (§ 61.109(a)(5) or (c)(4))
The PIC flight time requirements in the applicable aircraft category for a commercial pilot certificate with an airplane single engine land or helicopter rating. (§ 61.129(a)(2)(i) and (c)(2)(i))
The PIC flight time requirements for an ATP certificate with an airplane single engine land or helicopter rating (§ 61.159(a)(5) or § 61.161(a)(3))
(Next Slide)

## Slide 36: Flight Instructor Required Training and Endorsement in a Simplified Flight Controls Aircraft
Both part 61 subpart H and K flight instructors are required to obtain the make and model instructor qualifying endorsement prior to conducting flight instruction in that make and model of aircraft with the simplified flight controls designation. Subpart H flight instructors are required to take their initial flight instructor practical test in an aircraft with conventional flight controls as a prerequisite to instruct in an aircraft with simplified flight controls.
Regulations: § 61.195(m) and § 61.415(m).
Notes: We’ve discussed that pilots may obtain the required training an endorsement to act as PIC of an aircraft with a simplified flight controls designation from a flight instructor, but what does it take for a flight instructor to become qualified to provide this training? Simply put, a flight instructor must first meet the pilot qualification requirements for the make and model of aircraft in which they intend to provide that training.
Therefore, flight instructors (part 61 subpart H) and flight instructors with a sport pilot rating (part 61 subpart K) must obtain the make and model qualifying training and endorsement from another qualified flight instructor prior to conducting flight instruction in an aircraft with a simplified flight controls designation.
In addition to this pilot qualification, a flight instructor must also hold the appropriate category and class rating on their flight instructor certificate (for subpart H) or flight instructor privilege (for subpart K).
Finally, an applicant for a subpart H flight instructor certificate may not complete their initial flight instructor practical test in an aircraft with a simplified flight controls designation. An initial flight instructor practical test may only be accomplished in an aircraft with conventional flight controls.
(Next Slide)

## Slide 37: Sport Pilot Provisions Retained Under MOSAIC
General eligibility prerequisites
Option to use a U.S. driver's license in lieu of a medical certificate
Aeronautical experience requirements
Knowledge and flight proficiency requirements
Previous § 61.315 privileges and limitations
Notes: This discussion may be modified per Notes below based on the audience presented to.
We’ve discussed what is changing under MOSAIC, but let’s briefly review a few familiar sport pilot requirements that are retained under the new rules:
(1) General eligibility: The requirements to be at least 17 years old (16 for glider/balloon) and be English proficient are retained.
(2) Operating under a driver’s license: Under the new rules, a person may still exercise sport pilot privileges by operating an aircraft using a US driver’s license in lieu of a medical certificate. Unchanged with MOSAIC, that person must meet the requirements of 61.303(b), which require the pilot to:
(i) Comply with each restriction and limitation imposed by that person's U.S. driver's license and any judicial or administrative order applying to the operation of a motor vehicle;
(ii) Have been found eligible for the issuance of at least a third-class airman medical certificate at the time of his or her most recent application (if the person has applied for a medical certificate);
(iii) Not have had his or her most recently issued medical certificate (if the person has held a medical certificate) suspended or revoked or most recent Authorization for a Special Issuance of a Medical Certificate withdrawn; and
(iv) Not know or have reason to know of any medical condition that would make that person unable to operate an aircraft in a safe manner.
- One notable exception to operating using a US driver’s license are the optional night privileges previously discussed.
[Note: The presenter may wish to provide a detailed review of the other § 61.303 operating limits and endorsement requirements as a refresher].
(3) Aeronautical experience requirements: Aside from the newly added helicopter privileges, all other existing aeronautical experience requirements for each category and class remain the same under MOSAIC.
[Note: The presenter may wish to provide a detailed review of the other § 61.313 aeronautical experience requirements as a refresher].
(4) Knowledge and proficiency requirements: Aeronautical knowledge requirements are unchanged under the new rules and flight proficiency requirements were unchanged other than the addition of hovering maneuvers, applicable only to the new helicopter privileges.
[Note: The presenter may wish to provide a detailed review of the other § 61.309 aeronautical knowledge and § 61.311 flight proficiency requirements as a refresher].
(5) Previous § 61.315 privileges and limitations: Finally, the § 61.315 privileges and limitations were changed only to allow for the new optional privileges previously discussed in this briefing. All other previous privileges and limitations are retained under MOSAIC. This includes not acting as pilot in command of an aircraft while carrying more than one passenger or for compensation or hire.
[Note: The presenter may wish to provide a detailed review of the other § 61.315 privileges and limitations as a refresher].
(Next Slide)

## Slide 38: MOSAIC Part 91 Changes
Notes: As we have just reviewed, the new MOSAIC rules under part 61 retain several key sport pilot requirements, ensuring that the foundational skills and safety standards remain intact for pilots operating light-sport category aircraft.
Building on this foundation, let's now shift our focus to changes under MOSAIC for part 91 flight operations. Part 91 regulation revisions reflect the evolving landscape of general aviation and are designed to enhance safety and efficiency across various flight operations, accommodating new types of aircraft and refining or creating operational rules.
Let's take a closer look at some of these important changes to part 91 under MOSAIC . . .
(Next Slide)

## Slide 39: Changes to Part 91 – Flight Operations Effective Date October 22, 2025
Right-of-way rules for converging aircraft now include more categories of aircraft, including those with non-traditional forms of propulsion.
  Right-of-way rules retained under MOSAIC
  MOSAIC updates
  Aircraft right-of-way priorities
Regulation: § 91.113(d)
Notes: Although the majority of MOSAIC part 91 changes do not go into effect until July 24, 2026, there are three regulations that will become effective on October 22, 2025. These new operating rules involve expanding right-of way rules, improving operations in class G airspace, and clarifying the process for attaching a tow-hitch for eligible aircraft . . . Which will be presented on the following three slides:
First, the right-of-way rules outlined in § 91.113, specifically paragraph (d), focuses on converging aircraft and how these rules apply across different aircraft categories. MOSAIC still maintains that when aircraft of the same category are converging at approximately the same altitude (excluding head-on or nearly head-on situations), the aircraft on the other's right has the right-of-way. When the aircraft are of different categories, the right-of-way rules also still maintain the privilege of less maneuverable aircraft to safely proceed with priority over more maneuverable aircraft in the NAS. Pilots must be vigilant to see and avoid other aircraft; and as always, aircraft in distress have the right-of-way over all other air traffic.
However, now MOSAIC expands the categories of aircraft listed in the right-of-way rules by using the term “powered aircraft” instead of “engine-driven” to better convey the inclusion of aircraft that may have non-traditional forms of propulsion, including electric propulsion.
Balloons: Have the highest priority, with the right-of-way over any other category of aircraft due to their limited ability to maneuver.
Gliders: Have the right-of-way over powered aircraft, reflecting their reliance on natural forces for flight and limited maneuverability.
Airships: Have priority over all other powered aircraft, except for an aircraft towing or refueling other aircraft.
Towing or Refueling Aircraft: Hold the right-of-way over all other powered aircraft, given the precise nature of their operations.
(Next Slide)

## Slide 40: Changes to Part 91 – Flight Operations
Operations in Class G airspace involving the direction of aircraft turns are improved by:
  Including more aircraft by replacing “airplane” with “powered fixed-wing aircraft”
  Separating aircraft by operational needs, aircraft configurations, and speeds
  Enhancing avoidance of dissimilar aircraft
Regulation: § 91.126(b)
Notes: Second, MOSAIC has made improvements for operating on or in the vicinity of an airport in Class G airspace under § 91.126(b), specifically the direction of turns. Before MOSAIC, § 91.126(b) required that, when approaching to land at an airport without an operating control tower in Class G airspace, each pilot of a helicopter or a powered parachute must avoid the flow of fixed-wing aircraft. Unfortunately, this requirement only addressed helicopters and powered parachutes. It did not consider other types of aircraft that may require access to these airports, including emerging aircraft technologies.
So, MOSAIC now allows a wider range of aircraft and improves their separation by considering operational needs, aircraft configurations, and speeds. The intention is to mitigate the risk of collisions by effectively managing interactions between dissimilar aircraft.
Direction of Turns
When approaching to land at an airport in Class G airspace without an operational control tower:
1) Pilots of powered fixed-wing aircraft are required to make all turns to the left. However, if the airport displays approved light signals or visual markings indicating that turns should be made to the right, pilots must follow those instructions and make right turns.
2) Pilots of any other powered aircraft should ensure they do not interfere with the traffic flow of powered fixed-wing aircraft. Which remedies any concerns regarding non-powered aircraft operations. This is consistent with the guidance in AC-90-66C, Non-Towered Flight Operations, if both airplanes and gliders use the same runway, the glider traffic pattern should be inside the pattern of powered aircraft. Gliders may fly the same direction traffic pattern as powered aircraft in certain wind conditions and may use a separate, opposing direction traffic pattern in other wind conditions.
(Next Slide)

## Slide 41: Changes to Part 91 – Flight Operations
Tow-hitch installation​ process is clarified for eligible aircraft towing gliders and unpowered ultralight vehicles.
  Standard airworthiness certificate
  Special airworthiness certificate with type certificate
  Special airworthiness certificate without type certificate
Regulation: § 91.309(a)(2)
Notes: Lastly, let's delve into the clarifications regarding the tow-hitch installation process as specified in § 91.309(a)(2). These guidelines are crucial for aircraft involved in towing gliders and unpowered ultralight vehicles.
Aircraft with the following airworthiness types:
(i) Standard Airworthiness Certificate:
Aircraft with a standard airworthiness certificate must be equipped with a tow-hitch that has been approved by the Administrator. The installation must also meet the Administrator’s approval standards. This ensures that the equipment and its installation conform to established safety criteria.
(ii) Special Airworthiness Certificate with Type Certificate:
For aircraft holding a special airworthiness certificate, where a type certificate has been issued, the tow-hitch must be either approved or otherwise authorized by the Administrator. These aircraft require adherence to specific standards that validate the safety and reliability of the towing equipment.
(iii) Special Airworthiness Certificate without Type Certificate:
Aircraft with a special airworthiness certificate that have not been previously issued a type certificate must have a tow-hitch that is approved or otherwise deemed acceptable by the Administrator. The installation must also be acceptable to the Administrator. This provision ensures that even in the absence of a type certificate, safety is not compromised, and the towing setup is rigorously evaluated.
These detailed requirements underscore the importance of adhering to approved installation practices to maintain safety during towing operations. By specifying the conditions for different airworthiness certificates, the regulations ensure that all towing aircraft meet high safety standards.
(Next Slide)

## Slide 42: Changes to Part 91 – Flight Operations Effective Date July 24, 2026
Forthcoming part 91 rules and guidance changes to FAA Order 8130.2 (upcoming revision M) include new experimental aircraft operations:
    Densely populated areas
    Former military aircraft
Regulation: § 91.319 and conforming amendments in § 21.191
Notes: Now, looking ahead to MOSAIC’s second effective date of July 24, 2026, the next two slides will provide a brief list of some part 91 flight operational changes that will be in the upcoming “M” revision for the FAA Order 8130.2 - Airworthiness Certification of Aircraft.
New Experimental Aircraft Operations:
The Administrator now has the authority to issue operating limitations for certain aircraft with experimental airworthiness certificates to conduct operations over densely populated areas or in congested airways during all phases of flight.
Additionally, former military aircraft with experimental airworthiness certificates can now operate for new purposes, such as repositioning the aircraft for public aircraft operations. This broadens the scope for utilizing these aircraft efficiently and safely.
(Next Slide)

## Slide 43: Changes to Part 91 – Flight Operations Effective Date July 24, 2026
  Forthcoming part 91 rules and guidance changes to FAA Order 8130.2 (upcoming revision M) include new flight operations:
    Restricted category aircraft
    Light-sport category aircraft
    Space support vehicle flights
Regulation: § 91.313, § 91.327, § 91.331
Notes: In addition to new experimental aircraft operations in the upcoming FAA Order 8130.2 revision M, there will be new flight operations for restricted category, light-sport category aircraft, and for space support vehicle flights.
New Flight Operations:
Restricted Category Aircraft:
A restricted category aircraft cannot be operated for other than the special purpose for which it is certificated or other than an operation necessary to accomplish the work activity directly associated with that special purpose. MOSAIC does not change this restriction. Rather, MOSAIC now adds “exhibition” to the list in § 91.313 of operations that are considered necessary to accomplish the work activity directly associated with a special purpose operation. This change allows restricted category aircraft to fly to exhibitions, trade shows, and other events. Remember, that while at the exhibition event, these aircraft are still limited to the special purpose for which the aircraft is certificated. So, an aircraft may be limited to only a static display at such events.
Light-Sport Category Aircraft:
1) First, MOSAIC allows certain light-sport category aircraft that meet applicable consensus standards to perform certain aerial work operations for compensation or hire. Specifically, the new § 91.327(a)(3) permits certain light-sport category aircraft to conduct aerial work operations IF such operations are designated by the manufacturer and specified in the aircraft's pilot operating handbook or operating limitations, as applicable, and in the manufacturer's statement of compliance for the aircraft in accordance with § 21.190.
2) Second, MOSAIC specifies requirements for towing a glider or unpowered ultralight vehicle, in accordance with § 91.309 and § 21.190, for compensation or hire.
3) Third, for light-sport category aircraft the maximum airplane occupancy is 4. And, the maximum occupancy for other aircraft types is 2. As a reminder, sport pilots are still limited to carrying 2 occupants.
Experimental Aircraft Space Support Vehicle Flights:
Space support vehicle flight operations are now codified under MOSAIC, enabling certain experimental aircraft to conduct space support vehicle flights to simulate space flight conditions.
These operations can carry persons or property for compensation or hire without needing an air carrier certificate or exemption, expanding potential commercial and operational opportunities.
(Next Slide)

## Slide 44: MOSAIC Rule/Guidance References
To view the complete Modernization of Special Airworthiness Certification (MOSAIC) Final Rule use this link:
  Federal Register : Modernization of Special Airworthiness Certification
Guidance documents:
  FAA Order 8900.1 Volume 5, Chapter 2, Sections 12 & 24
  AC 61-65K Certification: Pilots and Flight and Ground Instructors
  AC 61-146 Pilot Certification and Operations for Sport Pilots, Flight Instructors with a Sport Pilot Rating, and Simplified Flight Controls.
Notes: The sources on this slide provide more detailed information on the MOSAIC rule and sport pilot (and flight instructor with a sport pilot rating) certification, privileges, and limitations.
eCFR is also not updated until the govt reopens so the only place to find the new regulations is on the link on the slide.
(Next Slide)

## Slide 45: Contact Information
If you have further questions, please email AFS 810 at:
9-afs-800-correspondence@faa.gov.
Please expect a 30 day turn around.
Notes: (Next Slide)

## Slide 46
Modernization of Special
Airworthiness Certification
(MOSAIC)
Federal Aviation
Administration
Notes: (The End)